## Slide 1
TRON PROGRAMMING CONTEST 2026 · DEVELOPMENT ENVIRONMENT / DEVELOPMENT TOOL
Real-Time Disaster Communication
& Priority Handling System
Priority-driven emergency alerting for real-time embedded systems, built on μT-Kernel 3.0 and the Renesas EK-RA8P1.
Report
Classify
Transmit
μT-Kernel
Alert
μT-Kernel 3.0 | Renesas EK-RA8P1 | Local, Internet-Independent Pipeline

## Slide 2
Not All Disaster Reports Are Equal
A fire report and a routine update should never wait in the same line.
THE PROBLEM
Disaster reports arrive with mixed urgency — fire, medical, road blockage, or routine updates.
Treating every message identically risks delaying the most critical alert behind less urgent ones.
Real-time systems need deterministic, priority-aware dispatch, not simple first-in-first-out queues.
Result: without priority-aware dispatch, a FIRE report can sit behind routine messages in a simple queue — costing the seconds that matter most.
OUR SOLUTION
A local, priority-aware disaster pipeline
Smartphone
Classify &
Prioritize
Ethernet
μT-Kernel
Mailbox
Priority
Alert
A free-text disaster report is classified, prioritized, and dispatched to μT-Kernel 3.0's priority mailbox on the EK-RA8P1 — entirely over a local network, with no cloud or Internet dependency.

## Slide 3
System Architecture
Six components, one deterministic path from smartphone to real-time alert.
Smartphone
User submits
report
phone_server.py
Flask web
interface
disaster_ai.py
Classify +
assign priority
Ethernet / RMAC
Scapy frame
to EK-RA8P1
μT-Kernel 3.0
Priority mailbox
dispatch
Tera Term
Alert
output
PC-side (phone_server.py + disaster_ai.py) handles ingestion and classification. The EK-RA8P1 executes deterministic, real-time priority processing under μT-Kernel 3.0 — keeping the RTOS core free of any variable-latency decision logic.

## Slide 4
Priority Mailbox: Real-Time Dispatch
μT-Kernel 3.0 dispatches by urgency, not arrival order.
FIRE
Priority 1
MEDICAL
Priority 2
ROAD
Priority 3
NORMAL
Priority 4
PREEMPTION IN ACTION
1st submitted “Community meeting scheduled for tomorrow.”
NORMAL · Priority 4
immediately followed by
2nd submitted “Ohh no fire.”
FIRE · Priority 1
FIRE is dispatched FIRST —
regardless of arrival order.

## Slide 5
AI Integration: Designed, Not Bolted On
A deliberate architectural position on where AI belongs in a real-time pipeline.
Today: Rule-Based Triage
disaster_ai.py performs deterministic keyword classification across FIRE, MEDICAL, ROAD, and NORMAL, directly driving priority assignment.
Why Deterministic Here
μT-Kernel 3.0's priority mailbox needs bounded, predictable latency. Variable-latency ML inference would introduce jitter into the real-time core.
Roadmap: AI-Informed Priority
Near-term: confidence-scored ML classifier. Mid-term: continuous priority scale. Long-term: LLM-based severity & urgency extraction.
AI belongs at the decision-input boundary — disaster_ai.py — not inside the real-time core.

## Slide 6
Demonstrated Results
Verified end-to-end on real hardware, across all four categories.
FIRE
Priority 1
“Ohh no fire”
MEDICAL
Priority 2
“Person is injured”
ROAD
Priority 3
“Road is blocked”
NORMAL
Priority 4
Normal information
Tera Term — FIRE demonstration
Received Disaster Ethernet frame: 60 bytes
Destination MAC: 00:11:22:33:44:55
Source MAC: 00:0E:09:86:93:93
EtherType: 0x0800
Payload length: 46
FIRE detected!
Sending priority message: P=1, FIRE ALERT
MESSAGE RECEIVED
Priority : 1
Message : FIRE ALERT

## Slide 7
Strengths & Roadmap
What the prototype proves today, and where it goes next.
WHAT WORKS TODAY
Full end-to-end pipeline verified on real hardware — phone to RTOS alert.
Local, Internet-independent operation — no cloud dependency.
Genuine preemptive priority dispatch, demonstrated under μT-Kernel 3.0.
Classification cleanly isolated in disaster_ai.py, ready for AI upgrade.
WHERE IT'S HEADED
AI-based, confidence-scored message classification.
Authenticated / encrypted Ethernet transport for alert payloads.
Load testing under high-volume, concurrent disaster reports.
Finer-grained, continuous priority scale beyond four fixed levels.

## Slide 8
Thank You
Real-Time Disaster Communication & Priority Handling System
μT-Kernel 3.0 · Renesas EK-RA8P1 · TRON Programming Contest 2026